## Slide 1
Vibrational Spectroscopy
H
H
O
Bend

## Slide 2
Diatomic Molecules
So far we have studied vibrational spectroscopy in the form of harmonic and anharmonic oscillators.
  Technically these models only apply to diatomic molecules
    We will still use them as tools to make analogies for the vibrational behaviour of bigger molecules
  The vib. spectra of diatomics are not very useful for forensic applications
    They are usually gasses
    The is only one peak!

## Slide 3
Polyatomic Molecules
The potential energy function for polyatomics is really complicated!
  Function of 3N coordinates
    N = #of atoms. i = {1,2,3,…,N}
    3 is for the atomic “displacements” in x, y and z:
“Equilibrium” (lowest energy) position of each atom
Atomic coordinate displacements

## Slide 4
Polyatomic Molecules
  Analogy with a diatomic:
x = spring stretch distance
V
x0 = “equilibrium bond length”

## Slide 5
Polyatomic Molecules
The potential energy function for polyatomics is really complicated!
Set = 0
Slopes at bottom of potential well = 0
Harmonic terms
Anharmonic terms. Assume displacements small so these = 0
0
0
0

## Slide 6
Polyatomic Molecules
Well, to good approximation potential energy function for polyatomics isn’t too bad:
Forces (force constants) to displace each atom “a little bit” around each of their equilibrium positions
PE is (approx.) a sum of coupled harmonic oscillators, like connected bed springs!

## Slide 7
Polyatomic Molecules
Can go a little further by finding sums of displacements that “don’t feel each other”
  The independent vibrations are called normal coordinates, Qi
  Normal coordinates “decouple” the harmonic oscillators:

## Slide 8
Normal Coordinates
For linear molecules there are always 5 normal coordinates = 0
For non-linear molecules there are always 6 normal coordinates = 0
  These correspond to translations and rotations!
  They are not vibrations!
For linear molecules there are 3N-5 vibrations
For non-linear molecules there are always 3N-6 vibrations

## Slide 9
Vibrational Schrodinger Equation
This is just a bunch of harmonic oscillator SEs
  Energy:
(approx) vibrational frequencies!
# of quanta in normal mode i
Insert the operators

## Slide 10
Vibrational Spectrum
The collection of wi is called the (harmonic) vibrational spectrum of the molecule!
  This is what we (basically) see in FT-IR for molecules with IR active normal modes (vibrations)
H2O: 3 normal modes, all IR active
2 more normal modes overlapped here
1 normal mode
Stuff not accounted for by harmonic model

## Slide 11
Vibrational Spectrum
What do the (approx) normal modes look like?
  Here theory helps us a lot. Modern quantum chemistry programs can easily spit out the Fi,j force constants, F
    Called the Hessian matrix
  F is 3N×3N
    x1, y1, z1, …, xN, yN, zN by x1, y1, z1, …, xN, yN, zN
  Diagonalizing F gives:
    Q Eigenvectors. What the normal modes look like!
    L Eigenvalues. Square root of these are the wi
QTFQ = L
In wavenumbers

## Slide 12
Vibrational Spectrum
Actually looking at Q to sketch the vibrations is a little difficult…. Best left to a computer.
  For H2O:
H
H
O
H
H
O
H
H
O
Symmetric Stretch
Bend
Asymmetric Stretch

## Slide 13
Mechanisms of Vibration
Typical fundamental vibrations of normal modes (vi = 0  vi = 1) have energies in the chunk of the infrared region:
  400 cm-1 – 4,000 cm-1
Normal mode Qi
V
vi = 0
vi = 1
is absorbed by the mode
g

## Slide 14
Mechanisms of Vibration
Typical fundamental vibrations of normal modes (vi = 0  vi = 1) have energies in the chunk of the infrared region:
  400 cm-1 – 4,000 cm-1
Source spectrum
Spectrum reaching the detector
Sample

## Slide 15
Mechanisms of Vibration
Raman Vibrational Scattering
vi = 1
vi = 2
vi = 0
vi = 1
vi = 2
vi = 1
vi = 2
Somewhere into the rainbow
e-
Elastic (Rayleigh) scattering:
Florescence
e-
Inelastic scattering:
Stokes
e-
Inelastic scattering:
Anti-Stokes

## Slide 16
Active Vibrational Modes
The “irreducible” vibrations of a molecule are its normal modes
In order for a vibrational mode to show up in a spectrum:
  IR active modes: vibration changes dipole moment of the molecule
  Raman active modes: vibration changes the polarizability (squishiness) the molecule
Dipole moment op. for IR
Polarizability op. for Raman

## Slide 17
Active Vibrational Modes
If molecule has a “center of symmetry” it has no common IR and Raman active nodes
C
OH
Cl
Cl
Cl
C
C
Cl
Cl
H
H
Has center of symmetry
Has no common IR and Raman active modes
Has no center of symmetry
Has some common IR and Raman active modes

## Slide 18
Infrared Vibrational Spectrocscopy
Vibrational spectroscopy in forensic science is done experimentally!
  Most common modern method is Fourier Transform Infrared (FT-IR) spectroscopy
Thermo-Nicolet
We’re going to focus on this part

## Slide 19
The Michelson Interferometer
Incoming wave
Beam spliter
Fixed mirror
Movable mirror
dmax
dmin
d-axis
d0=0

## Slide 20
Incoming wave
split
Path lengths equal
Recombine in-phase
Fixed mirror
Movable mirror
recombine
The Michelson Interferometer

## Slide 21
Incoming wave
split
Path lengths NOT equal
Recombine out-of-phase
Fixed mirror
Movable mirror
recombine
The Michelson Interferometer

## Slide 22
What does an Michelson interferometer do to source light with 1 wavelength component?
  This is what the detector records:
Zooming in
The Michelson Interferometer

## Slide 23
What does an Michelson interferometer do to source light with 1 wavelength component?
  This is what the detector records:
Zooming in
One complete cycle at d = l
650 nm
The Michelson Interferometer
Trick: A laser can give us the mirror position, d, very accurately!

## Slide 24
Interferograms
What does an Michelson interferometer do to source light with 1 wavenumber component?
  This is what the detector records (zoomed in):

## Slide 25
What does an Michelson interferometer do to source light with 2 wavenumber components?
  This is what the detector records (zoomed in):
Interferograms

## Slide 26
What does an Michelson interferometer do to source light with 3 wavenumber components?
  This is what the detector records (zoomed in):
Interferograms

## Slide 27
What does an Michelson interferometer do to source light with 10 wavenumber components?
  This is what the detector records (zoomed in):
Interferograms

## Slide 28
What does an Michelson interferometer do to source light with 20 wavenumber components?
  This is what the detector records (zoomed in):
Interferograms

## Slide 29
What does an Michelson interferometer do to source light with 50 wavenumber components?
  This is what the detector records (zoomed in):
Interferograms

## Slide 30
What does an Michelson interferometer do to source light with 100 wavenumber components?
  This is what the detector records (zoomed in):
Interferograms

## Slide 31
What does an Michelson interferometer do to source light with 500 wavenumber components?
  This is what the detector records (zoomed in):
Interferograms

## Slide 32
What does an Michelson interferometer do to source light with 1000 wavenumber components?
  This is what the detector records (zoomed in):
Interferograms

## Slide 33
Sample
FT-IR Vibrational Spectroscopy
Absorbance spectrum
Source spectrum
FFT

## Slide 34
We now know that the interferogram is a sum of waves:
  One wave for each cm-1 in the source spectrum: multiplex
Fourier Transform of the Interferogram
  Some of the multiplexed information in the source’s interferogram is absorbed by the sample’s vibrations
    Whole vibrational spectrum is recorded in a sweep of the interferometer’s mirror!

## Slide 35
Fourier Transform of the Interferogram
  How do we untangle the interferogram to see which parts of the spectrum got absorbed?
  A little fancier version of the interferogram’s equation is:
Here is our IR spectrum inside
  To get it out, invert the equation with a Fourier transform:

## Slide 36
FT-IR Vibrational Spectroscopy
Simulation for IR-active modes of CH4