## Slide 1
Signal Processing and Statistical Tools
In the Forensic Sciences

## Slide 2
  Daubert (1993)- Judges are the “gatekeepers” of scientific evidence.
  Must determine if the science is reliable
    Has empirical testing been done?
      Falsifiability
    Has the science been subject to peer review?
    Are there known error rates?
    Is there general acceptance?
  Federal Government and 26(-ish) States are “Daubert States”
The Daubert Standard

## Slide 3
Jerry Petillo
KM
KNM
Tool Mark Comparison Microscope

## Slide 4
  Generate many standard reproducible striation patterns for each screwdriver.
    Modeling clay used as impression medium

## Slide 5
  Measure line/grove positions from edges of patterns
  Descritize width of pattern into 0.05 mm increments
    In list 140 increments long (7 mm) record 1 if line/grove in a box, 0 otherwise
      Gives 140-dimentional feature vectors for each pattern

## Slide 6
Automated Identification Striations on Digital Images
J. Speir

## Slide 7
Data Acquisition For Toolmarks
Confocal Microscope
Focus Variation Microscope

## Slide 8
9mm Glock fired cartridge cases
Bottom of
Firing pin imp.

## Slide 9
Surface Data
37.88 | 37.89 | 37.89 | 37.90 | 37.92 | 37.91 | 37.93 | 37.93 | 37.94 | 37.99
37.88 | 37.89 | 37.87 | 37.87 | 37.87 | 37.85 | 37.89 | 37.92 | 37.97 | 38.02
37.86 | 37.85 | 37.84 | 37.84 | 37.84 | 37.85 | 37.85 | 37.92 | 37.98 | 38.03
37.84 | 37.82 | 37.81 | 37.81 | 37.83 | 37.85 | 37.88 | 37.92 | 37.97 | 38.04
37.81 | 37.80 | 37.80 | 37.82 | 37.84 | 37.86 | 37.89 | 37.94 | 37.98 | 38.05
37.81 | 37.78 | 37.79 | 37.82 | 37.85 | 37.89 | 37.94 | 37.96 | 38.00 | 38.04
37.82 | 37.80 | 37.80 | 37.83 | 37.87 | 37.91 | 37.98 | 37.99 | 38.02 | 38.05
37.84 | 37.81 | 37.80 | 37.81 | 37.84 | 37.89 | 37.95 | 37.99 | 38.01 | 38.06
37.84 | 37.80 | 37.76 | 37.77 | 37.78 | 37.86 | 37.92 | 37.96 | 38.00 | 38.03
37.80 | 37.77 | 37.76 | 37.74 | 37.79 | 37.84 | 37.90 | 37.93 | 37.98 | 38.00
Surface heights (mm)
Land Engraved Area:
Signal is “double precision”: 64-bits/points sampled at given resolutions

## Slide 10
Shear marks on primer of two different Glock 19s

## Slide 11
  3D tool mark data usually needs (a lot of…) preprocessing
Steps in Processing Surface “Signal” Data
Possibly remove “long range”
behavior (leveling, form removal)
Crop out areas of interest

## Slide 12
Bullet base, 9mm Ruger Barrel
Bullets
LEA

## Slide 13
2D profiles
3D surfaces
(interactive)
Screwdriver Striation Patterns in Lead

## Slide 15
  Think of a toolmark surface as being made up of a series of waves
Surface Filtering

## Slide 16
  Examine different scales by “blocking out” (filtering) some of the sinusoids
Surface Filtering
“Low Pass” filter blocks
high frequencies
and passes low frequencies
(long wavelengths)

## Slide 17
  Examine different scales by “blocking out” (filtering) some of the sinusoids
Surface Filtering
“High Pass” filter blocks low frequencies
and passes high frequencies
(short wavelengths)

## Slide 18
  Wavelength “cutoffs”
Surface Filtering Trivia
A “High Pass” filter
A “Low Pass” filter
lcut
lcut
Wavelength ranges
  Short wavelengths passed: roughness
  Medium wavelengths passed: waviness
  Long wavelengths passed: form

## Slide 19
  Band-pass filter: Select narrow wavelength bands to keep.
    High-pass/Low-pass combinations (Filter banks)
    Wavelets are great at doing this
Surface Filtering with Wavelets

## Slide 20
We can simulate profiles as well
Profile Simulator
Based on DWT MRA
  May shed light on the processes which generate the surfaces

## Slide 21
Wavelet based simulator for 2D toolmarks:
2D Simulations with Wavelets
LH4
HL4
HH4
+
Simulate stochastic detail

## Slide 22
  Gauge similarity between tool marks with one number
    Similarity “metric” is a function which measures “sameness”
      Only requirement: s(A,B) = s(B,A)
      There are an INFINITE number of ways to measure similarity!!
  Often max CCF is used.
How to Compare Signals?

## Slide 23
Known Match (KM) example:

## Slide 24
KNM can sometimes have high max-ccf…
max-ccf: 0.751

## Slide 25
Univariate approaches compute estimates of similarity score distributions for Known Matches (KM) and Known Non-Matches (KNM)
Pair-Wise Comparisons
#False Non-matches/#KM-Comparisons = FNMR
#False Matches/#KNM-Comparisons = FMR
Error rate = (#False Non-matches + #False Matches)/#Comparisons
KNM similarity score distribution
KM similarity score distribution
Cut-off
Call: Matches
Call: Non-Matches

## Slide 26
KNM1=KM1
KNM2
Compare “lines” KNM1 vs. KNM2
KM1
KM2
Compare “lines” KM1 vs. KM2
KM matching lines
and scores
KNM matching lines
and scores

## Slide 27
A tool mark is a “word” in a chapter.
A line is a “letter” in a “word”
Take a representative for a group of tool marks
made by the same tool as a “chapter” in a “dictionary”

## Slide 28
1740 Toolmarks (screwdriver striation profiles)
from database and simulation
Biasotti-Murdock Dictionary
(58 “chapters”)
Consecutive Matching Striae (CMS)-Space

## Slide 29
How many PCs should we use to represent the data??
    No unique answer
FIRST we need an algorithm to I.D. a toolmark to a tool
  3D PCA of 1740 real and simulated Biasotti-Murdock’d striation patterns from 58 screwdrivers:
  ~9% variance retained

## Slide 30
Support Vector Machines
    Support Vector Machines (SVM) determine efficient association rules
      In the absence of specific knowledge of probability densities
SVM decision boundary

## Slide 31
  How many Principal Components should we use?
PCA-SVM
With 7 PCs, expect ~3% error rate
With 13 PCs, expect ~1% error rate

## Slide 32
  Cross-Validation: hold-out chunks of data set for testing
    Known since 1940s
    Most common: Hold-one-out
Error Rate Estimation
  Bootstrap: Randomly selection of observed data (with replacement)
    Known since the 1970s
    Can yield confidence intervals around error rate estimate
  The Best: Small training set, BIG test set

## Slide 33
How good of a “match” is it?
Conformal PredictionVovk
Data should be IID but that’s it
Cumulative # of Errors
Sequence of Unk Obs Vects
80% confidence
20% error
Slope = 0.2
95% confidence
5% error
Slope = 0.05
99% confidence
1% error
Slope = 0.01
Can give a judge or jury an easy to understand measure of reliability of classification result
This is an orthodox “frequentist”
approach
    Roots in Algorithmic Information Theory
Confidence on a scale of 0%-100%
Testable claim: Long run I.D. error-rate should be the chosen significance level

## Slide 34
Conformal Prediction
Theoretical (Long Run)
Error Rate: 5%
Empirical Error Rate: 5.3%
14D PCA-SVM Decision Model
for screwdriver striation patterns
For 95%-CPT (PCA-SVM) confidence intervals will not contain the correct I.D. 5% of the time in the long run
  Straight-forward validation/explanation picture for court

## Slide 35
    An I.D. is output for each questioned tool mark
      This is a computer “match”
    What’s the probability the tool is truly the source of the tool mark?
    Similar problem in genomics for detecting disease from microarray data
      They use data and Bayes’ theorem to get an estimate
How good of a “match” is it?
Efron Empirical Bayes

## Slide 36
Empirical Bayes
From Bayes’ Theorem we can getEfron:
Estimated probability of not a true “match” given the algorithms' output z-score associated with its “match”
Names: Posterior error probability (PEP)Kall
Local false discovery rate (lfdr)Efron
Suggested interpretation for casework:
= Estimated “believability” that the specific tool
produced the tool mark

## Slide 37
Use locfdrlocfdr
Fit classic Poisson regression for f(z)
Use modified locfdr/JAGSJAGS,Plummer or StanStan
Fit Bayesian hierarchical Poisson regressions
z
z
Fit local-fdr models

## Slide 38
JAGS MCMC Bayesian over-dispersed Poisson with intercept, on test set
A Bayesian Hierarchical Model: Believability Curve
95% HPDI
“uncertainty bands”

## Slide 39
Empirical Bayes’
  Model’s use with crime scene “unknowns”:
This is the est. post. prob. of no association = 0.00027 = 0.027%
Computer outputs “match” for:
unknown crime scene toolmarks-with knowns from “Bob the burglar” tools
This is an uncertainty in the estimate

## Slide 40
  R is not a black box!
    Codes available for review; totally transparent!
  R maintained by a professional group of statisticians, and computational scientists
    From very simple to state-of-the-art procedures available
    Very good graphics for exhibits and papers
  R is extensible (it is a full scripting language)
    Coding/syntax similar to MATLAB
    Easy to link to C/C++ routines
Why ?

## Slide 41
  Where to get information on R :
    R: http://www.r-project.org/
      Just need the base
    RStudio: http://rstudio.org/
      A great IDE for R
      Work on all platforms
      Sometimes slows down performance…
    CRAN: http://cran.r-project.org/
      Library repository for R
      Click on Search on the left of the website to search for package/info on packages
Why ?

## Slide 42
Finding our way around R/RStudio